## Slide 1
2016 Year-End Meeting
Rolls-Royce, Indianapolis, IN
Dec. 14-16, 2016
EAR 99 – Non-Proprietary
Turbulent Flame Speed of Large Hydrocarbon Fuels
David Blunck, Oregon State University
Acknowledgments: Aaron Fillo (funding from NSF), Jonathan Bonebrake, Nathan Schorn,

## Slide 2: ST Task
Identify fuel sensitivity of turbulent flame speeds at atmospheric and sub-atmospheric conditions
Measure boundary conditions
How do turbulent flame speed measurements relate to LBO?
LBO depends on ST
ST measurements provide insight into stability….
without the complications of complex fluid mechanics and two-phase flows
Objectives

## Slide 3: Experimental Approach
- Abel Transform centerline
- Progress Fit (c)
Re | U | u'rms (a) | u'rms (b)
5000 | 13.7 | 1.8 | 2.6
7500 | 20.6 | 2.7 | 3.9
10000 | 27.5 | 3.6 | 5.2
Flow velocity and turbulence intensity (m/s)
H
R
H
200 nm ≤ λ ≤ 800 nm ICCD data
ICCD
Axi-symmetric
Abel Transform
Filtered
Raw
Burner schematic [Fillo]
(a) Low turbulence intensity(TI) (~13%)
(b) High turbulence intensity (TI) (~19%)
Turbulence Generator
Designs from Georgia Tech and AFRL gratefully acknowledged
Preheat Temperature: 470 K

## Slide 4: ST at Atmospheric Conditions
C1
C5, A2
C1, C5
A2
A2, C5
C1
Indicates fuel is breaking through the flame front for lower Φ
RMS IR: Re = 5000
Φ =1
Φ =0.9
Φ =0.8, 0.7
Relationship to LBO
Lower flame speeds and reduced stability for C1 make flames more prone to blowoff
Similar flame speeds for C5 and A2 tend to support similar LBO conditions

## Slide 5: Sensitivities of C1
Upstretched laminar flame speeds at 400K
The slower flame speed for C1 will make more sensitive to blowoff
Greater sensitivity of C1 to flame stretch makes flame less stable
Similar stretch sensitives and flame speeds for C5 and A2 suggest both would have similar blowoff
Sensitivity to velocity fluctuations
Sensitivity to global stretch

## Slide 6: Pressure Sensitivity of ST
Re = 7,500
0.6 atm
1 atm
Flame in pressure vessel
Different sensitives of ST to pressure for the fuels indicate that blowoff characteristics may change

## Slide 7: Future Work
Complete test matrix of subatmospheric data collection
Collect measurements of ST for surrogates and fuel blends
Complete measurements of turbulence conditions and identify stability thresholds